## Slide 1: SMART INDIA HACKATHON 2026
iTantra
Problem Statement ID – SIH26173
Problem Statement Title- iTantra
Problem Statement- Indian Multilingual TTS & STT Aided Neural Transceiver Radio Access for low bitrate links
Software Theme-Smart Automation
PS Category- Software
Team ID- 165027
Team Name- GIT BIT
Git Bit

## Slide 2: SMART INDIA HACKATHON 2026
THE PROBLEM + CORE INSIGHT
iTANTRA keeps the human experience as voice, but moves only compact information across the constrained link.
FIELD / DISTRESS SCENARIO
Continuous voice is data-heavy
Low-bitrate links cannot carry rich audio reliably
Users still need spoken output for accessibility
ITANTRA APPROACH
Keep VOICE at both ends. Send only COMPACT TEXT in between.
1
Speech
2
STT + pause detection
3
Compact text packet
4
Wi‑Fi / Bluetooth
5
TTS
6
Voice
10 INDIAN LANGUAGES — ONE COMMON PIPELINE
Hindi
Gujarati
Marathi
Kannada
Malayalam
Tamil
Telugu
Odia
Bengali
English
Core SIH alignment:
Speech → local STT → compact text → local TTS
Optional translation is an enhancement — not the core transport.
2/6
Git Bit
Unlike push-to-talk radios or VoIP apps, iTantra reconstructs speech from a few bytes of text — fully offline, with no SIM or internet needed.

## Slide 3
SMART INDIA HACKATHON 2026
3/6
One lightweight architecture for 10-language voice communication over constrained links.
NODE A
Android
NODE B
Android
STT
10 languages
TXT
compact packet
P2P LINK
Bluetooth RFCOMM Wi‑Fi Direct TCP AES‑GCM secured
TTS
10 languages
FEASIBILITY PROOF POINTS
✓
Offline operation
STT/TTS models run on device
✓
Low payload
Voice converted to compact text
✓
Field modes
PTT and continuous conversation
✓
Emergency alert
Priority compact codes + playback
✓
Security
SAS verified encrypted session
✓
Practical hardware
Standard Android devices
Demo metrics to show: STT accuracy/WER • packet size saved vs audio • latency • RAM • two-phone delivery test
Git Bit
TECHNICAL APPROACH & FEASIBILITY
RISKS & MITIGATION
STT accuracy VAD noise gating + confidence threshold; flag low-confidence phrases for repeat.
Short range ACK/retry improves reliability; LoRa relay path is scoped for future range extension.
10-language models Load only the selected language pack at runtime to reduce RAM/storage pressure.
Battery drain VAD gates STT/TTS so processing runs during speech instead of continuously.

## Slide 4: SMART INDIA HACKATHON 2026
IMPACT + DEPLOYMENT
WHO NEEDS iTANTRA — AND WHY IT MATTERS
REMOTE / LOW-CONNECTIVITY FIELD
VOICE IN
→
TINY DATA
→
VOICE OUT
The receiver still hears speech; the link only carries compact information.
DEPLOYMENT SCENARIOS
Disaster response
Remote rescue
Forest operations
Maritime / field teams
Industrial emergencies
Security operations
10-LANGUAGE EXPERIENCE
Speak in any supported language → compact text moves → speech is reconstructed at the receiver.
Accessible
Spoken output
Efficient
Less radio payload
Private
Local processing
Practical
Existing Android devices
4/6
Git Bit

## Slide 5
SMART INDIA HACKATHON 2026
SYSTEM ARCHITECTURE
HOW iTANTRA WORKS — END TO END
CORE OFFLINE PIPELINE
MIC
Speech
VAD
Pause / stop detection
STT
10-language STT
TXT
Compact packet
P2P
Bluetooth / Wi‑Fi Direct
TTS
10-language TTS
SPK
Voice out
OPERATING MODES
PTT ON
Walkie‑talkie style push-to-talk
PTT OFF
Phone-like continuous conversation
ALERT
Priority emergency playback
SECURE SESSION
ECDH • SAS • AES‑GCM
OPTIONAL FUTURE RANGE EXTENSION
Android Phone
Heltec WiFi LoRa 32 V3
LoRa Link
Heltec WiFi LoRa 32 V3
Android Phone
FUTURE / OPTIONAL
5/6
Git Bit

## Slide 6: SMART INDIA HACKATHON 2026
Git Bit
• SIH26173 – iTantra: https://sih.gov.in/sih2026PS
• ISRO: https://www.isro.gov.in/
• Android Developers: Kotlin & Android APIs
• Oracle Java: Java & JVM documentation
• Gradle: Build automation & dependency management
• Python: AI & speech-processing components
• Research Focus: Multilingual STT + TTS + low-bandwidth communication
• Project Repository: https://github.com/avira-l07/workfix
REFERENCES & PROJECT