## Slide 1: SMART INDIA HACKATHON 2026
iTantra
Problem Statement ID – SIH26173
Problem Statement Title- iTantra
Problem Statement- Indian Multilingual TTS & STT Aided Neural Transceiver Radio Access for low bitrate links
Software Theme-Smart Automation
PS Category- Software
Team ID- 165027
Team Name- GIT BIT
Git Bit
Notes: SIH26173 submission pitch, updated 5 October 2026. Six-slide template, team GIT BIT and Team ID 165027 retained. Official requirement: https://sih.gov.in/sih2026PS. Capability descriptions reflect current implementation; the labelled delivery plan describes forthcoming demo and release milestones, not completed phone validation.

## Slide 2: SMART INDIA HACKATHON 2026
THE PROBLEM + CORE INSIGHT
iTANTRA brings spoken communication to constrained links through local speech AI and compact text transport.
FIELD / DISTRESS SCENARIO
Continuous voice is data-heavy
Low-bitrate links cannot carry rich audio reliably
Users still need spoken output for accessibility
ITANTRA APPROACH
Keep VOICE at both ends. Send only COMPACT TEXT in between.
1
Speech
2
STT + pause detection
3
Compact text packet
4
Wi‑Fi / Bluetooth
5
TTS
6
Voice
TEN LANGUAGES. ONE OFFLINE SPEECH PIPELINE.
Hindi
Gujarati
Marathi
Kannada
Malayalam
Tamil
Telugu
Odia
Bengali
English
Core design:
Speech -> local STT -> compact text -> local TTS
Selected speech packs run locally after initial model download.
2/6
Git Bit
On-device speech processing and direct Bluetooth / Wi-Fi Direct transport keep the core voice flow independent of cloud inference.
Notes: Sources: docs/QUICK_STAT_SUMMARY.md; docs/LANGUAGE_BENCHMARKS.md; local Android implementation. Runtime: https://k2-fsa.github.io/sherpa/onnx/index.html. Ten language packs are selectable; speech inference runs locally after initial download. The core peer transport is Bluetooth RFCOMM or Wi-Fi Direct TCP. General cross-language translation is an optional extension and has language-pair restrictions. Photographs are representative illustrations retained from the supplied template.

## Slide 3
SMART INDIA HACKATHON 2026
3/6
Kotlin / Compose + sherpa-onnx: local speech processing and encrypted direct peer links.
NODE A
Android
NODE B
Android
STT
Selected pack
TXT
compact packet
P2P LINK
Bluetooth RFCOMM Wi‑Fi Direct TCP AES‑GCM secured
TTS
Selected voice
APPLICATION FEATURES
✓
Local speech
STT/TTS after model provisioning
✓
Text transport
Compact messages instead of audio
✓
Speech modes
PTT and pause-delimited segments
✓
Emergency alert
Four compact SOS codes + playback
✓
Encrypted peers
ECDH / SAS / AES-GCM session
✓
Local history
Room / SQLCipher storage
Demo flow: pair two Android devices -> push to talk -> encrypted text -> local voice playback
Git Bit
TECHNICAL APPROACH & FEASIBILITY
DESIGN CHOICES
Speech clarity
Pause detection creates speech segments. Dedicated language models handle recognition.
Reliable delivery
Direct Bluetooth / Wi-Fi links use message acknowledgements and retry.
Selective packs
Download the chosen language pack; speech model weights are managed separately from the APK.
Resource control
VAD gates speech processing. Diagnostics expose timing and runtime counters.
Notes: Implementation: Kotlin/Compose UI, sherpa-onnx STT/TTS, Room/SQLCipher history, ECDH/SAS/AES-GCM peers, PTT and pause-delimited speech, four compact SOS codes, acknowledgements/retries and diagnostics. Demo flow describes the intended two-device evaluation sequence. Device memory/CPU/battery and full audible delivery timing will be measured during that sequence. An external radio gateway and mesh are separate future extensions.

## Slide 4: SMART INDIA HACKATHON 2026
MEASURED PROGRESS + DEMO PLAN
MEASURED PROGRESS & SUBMISSION PLAN
REMOTE / LOW-CONNECTIVITY FIELD
10 LANGUAGES
→
454 TESTS
→
LOCAL AI
454 unit tests passed. Benchmarks cover ten languages; the Tamil GPU baseline provides the next training reference.
MEASURED RESULTS
Hindi WER 9.1%
English WER 6.9%
Tamil CTC WER 20.05%
Tamil RNNT WER 18.53%
Marathi TTS 181 ms
Tamil data overlap: 0
BENCHMARK CONTEXT
Hindi/English: desktop WER. Tamil: source GPU WER. 30 clips per set. Marathi: desktop synthesis-only mean.
Accuracy 40%
WER + speech quality
Efficiency 20%
APK / RAM / CPU
Latency 20%
Speech + delivery time
Demo plan
Two-device voice flow
4/6
Git Bit
Notes: Measured sources: docs/QUICK_STAT_SUMMARY.md and docs/LANGUAGE_BENCHMARKS.md; received itantra_tamil_pilot_reports (2).zip, retained under tools/stt_results/tamil-gate-b-training-process-review-2026-10-05/received-reports.zip. Latest recorded unit run: 454 tests, zero failures. Hindi/English desktop INT8 WER: 9.1% / 6.9% over 30 clean FLEURS validation recordings per language. Tamil original source-model GPU CTC WER 20.0507614213%, RNNT WER 18.5279187817%, Tamil script 30/30, same protected 30 recordings. These GPU results are baseline measurements, not fine-tuning gains or Android results. Marathi Piper synthesis mean 181 ms across 30 short phrases; excludes playback/transport and uses a desktop. Tamil saved-data guard checked 4,983 rows with zero overlaps/errors. The official criteria list accuracy 40%, efficiency 20%, latency 20%; no additional allocation is invented.

## Slide 5
SMART INDIA HACKATHON 2026
SYSTEM ARCHITECTURE
HOW iTANTRA WORKS — END TO END
CORE OFFLINE PIPELINE
MIC
Speech
VAD
Pause / stop detection
STT
Selected
STT pack
TXT
Compact packet
P2P
Bluetooth / Wi‑Fi Direct
TTS
Selected
TTS voice
SPK
Voice out
OPERATING MODES
PTT ON
Walkie‑talkie style push-to-talk
PTT OFF
Speech segments after pauses
ALERT
Priority alert playback
SECURE SESSION
ECDH • SAS • AES‑GCM
FINAL DEMO DELIVERY PLAN
Tamil tuning
Train / dev selection
Locked WER tests
ONNX / INT8 checks
Two-phone demo
SIGNED RELEASE
5/6
Git Bit
Notes: The upper pipeline and operating modes reflect current application code. The lower row is explicitly a future delivery plan: Tamil tuning, train/dev selection, locked held-out tests, ONNX/INT8 comparisons, two-device demo and signed release. Received GPU baseline passed; first training process stopped without a traceback or recorded exit code. A diagnostic retry is prepared. Training completion, general accuracy gains and signed release are forthcoming milestones.

## Slide 6: SMART INDIA HACKATHON 2026
Git Bit
• Official problem SIH26173: sih.gov.in/sih2026PS
• Offline speech runtime: sherpa-onnx for Android
• STT: IndicConformer / English FastConformer
• TTS: MMS-VITS / Marathi Piper voice
• Speech benchmarks: FLEURS, 30 clips per language
• Tamil data: Kathbath, 4,428 train / 555 dev clips
• Validation design: speaker-separated splits + locked tests
• Delivery sequence: model tuning -> demo -> signed APK
REFERENCES & DELIVERY APPROACH
Notes: Primary sources: https://sih.gov.in/sih2026PS; https://k2-fsa.github.io/sherpa/onnx/index.html; https://huggingface.co/ai4bharat/indicconformer_stt_ta_hybrid_ctc_rnnt_large; https://huggingface.co/datasets/google/fleurs; https://huggingface.co/datasets/ai4bharat/Kathbath. Local evidence: docs/LANGUAGE_BENCHMARKS.md, docs/QUICK_STAT_SUMMARY.md, docs/TAMIL_PILOT_REPORT_REVIEW_2026-10-05.txt. Kathbath split: 4,428 train / 555 dev clips, 123 / 14 speakers, 8.882 / 1.118 hours. Model-specific licensing and redistribution terms are reviewed as part of release preparation. This slide describes delivery methodology, not an assertion that all release milestones have already passed.